## Slide 1: LIS Admin Presented by Peggy Steele and Jane Blackmar Lab Implementation

## Slide 2: Printer Installation

## Slide 3: Printer Installation
Very general steps to setting up a printer:
  Add IP address to the etc/hosts file or config.sys file
  Add the queue to the config file (definition of the physical queue on the UNIX server)
  Add the printer to the printerc file (link between printer name defined in SCC modules and the printer queue defined on the UNIX server)
  Add the printer to the appropriate Users/Roles, and Sites using Security Management
Notes: SCC does the first three. Client does the last one

## Slide 4: Printer Installation
Type, Brand and Model of the printer.
Type of connection to the LIS
  Terminal Server
  Jet Direct
  Network
Other Requirements
  IP address
  Port ID (if needed)
  Gateway address (if needed)
  Name (first three characters must be unique)
Notes: To get a printer queue made

## Slide 5: Maintenance

## Slide 6: Maintenance
Check console messages/Monitor email for SPN
Check printer status
Check Remote Printing Modem and Fax Logs and Status
Check Interfaces and possible trace files
Check error logs, specifically ADT, OEHIS, and SFS
Check email for TMS task updates, and Backup Status.

## Slide 7: Maintenance
Check console messages/Monitor email for System Problem Notification (SPN) system.
Check printer status
Check Remote Printing Modem and Fax Logs and Status
Check Interfaces and possible trace files
Check error logs, specifically ADT, OEHIS, and SFS
Check email for TMS task updates, and Backup Status.
Notes: More periodic maintenance. Subsequent slides describe how to perform

## Slide 8: Maintenance- Check Printer Status
Tools>Utilities>Check Printers
  Displays all queues in a Not Ready Status
Tools>Utilities>Printer Status
  Displays status of all printers defined in printerc
Cancel, restart, or both cancel and restart the print jobs
Perform on both MAIN and AUX

## Slide 9: Maintenance- Remote Printing Status
Several times per day
Interfaces-> Remote Printing-> Fax Failed Logs

## Slide 10: Maintenance- Interface Status
  Interface>All Interfaces>Status Screen

## Slide 11: Maintenance Bridging to AUX
Notes: Look at interface setup on both MAIN and AUX.

## Slide 12: Maintenance- Accessing Trace Files
Notes: Go to Interface Setup, click on the black shoe prints. Make sure the interface/server is running. Select the correct day’s file.

## Slide 13: Maintenance- Accessing Trace Files
Notes: In 4.5, the trace files are very large and it is difficult to load the entire trace file much less look at it. To overcome this, you are first presented with a search screen. Enter the info you are searching for. The system will return every instance where that info is discussed plus the 5 lines about and 20 lines after. You can increase the number of lines if you want to.
The second line is about the tail of the trace- you can see the last 80 lines (by default) of the file. You can also change the number of lines here.
To see the entire file, do not enter anything and just hit search. But don’t be surprised if the file is too huge to open!

## Slide 14: Maintenance- Backups
Backup Types
  Database (Aux only):
    Daily
    Includes database, configuration files and dictionary files for each application.
    patient data (daily changes)
  Software: (AUX)
    At least once/month. Twice if in Implementation. After new software load.
    Application, executable, configuration
  Operating System (MAIN and AUX):
    Monthly. Before/After change to operating system
    AIX (also called mksysb by IBM)

## Slide 15: System Problem Notification (SPN)

## Slide 16: SPN
Preventive system monitoring service
Messages directed to SCC personnel
TMS task created to address any issues.
Three levels
  Alarm- immediate threat to system stability
  Warning- attention needed
  Notice- potential threat
Categories
  System
  Product
Notes: Soft will notify you of any SPN’s and what is being done about them via the task system.

## Slide 17: HIS Interface Communication

## Slide 18: 5 major interfaces models
ADT
Inbound Order Entry
Outbound Order Entry
Result Reporting
Billing
Notes: • ADT Admission, Discharge and Transfer– Relays information regarding Patient Demographics and Stay information.
• HISOE/ESB-OE Inbound Order Entry – Sends orders from the HIS to the LIS.
• Outbound Order Entry – Sends orders originating in SCC to the HIS.
• ESB-RR Result Reporting– Transmits results to the HIS.
• Billing – SCC formats and transmits charge information to the HIS.

## Slide 19: Communication with HIS accomplished through two or three connections:
RCV
SND
BILLS
Notes: • RCV Receiving interface - Receives data in real time from a foreign system and passes the information to ADT and inbound order entry.
• SND Sending interface– Sends outbound formatted data such as outbound orders and results to a foreign system. May also send charges.
• BILLS Billing interface – sends formatted charge files to a designated address by file transfer protocols.

## Slide 20
Notes: This is how 4.0 communicates with the HIS

## Slide 21
ESB Interface Overview (4.5)
Notes: How 4.5 communicates with the HIS

## Slide 22: HL7 Standards

## Slide 23: HL7 Standards
Developed in 1987
Health Level 7
Provides data communication standards for healthcare industry.
Packaged in the form of messages
  Message Type – defines message purpose
  Event Code – describes event that caused the message.
  Segments.- logical group of data making up message
  Fields.- collection making up segment

## Slide 24: HL7 Standards- Message Type
ADT – admission, discharge, transfer, merge
ORM – orders, cancellations, order status changes
ORU – results of orders
DFT – financial

## Slide 25: HL7 Standards- Trigger Events
ADT Events - admitting a patient
Order Events - creating an order
Result Events - entry of a result
Financial Events – transmitting a charge for a service

## Slide 26: HL7 Standards- Segment
Has a defined structure
Is identified by a unique 3-character code.
Is comprised of a specific set of related fields.
May occur with the message once or many times.
May be required or optional depending on HL7 standards.
Ends with special characters, usually \r.

## Slide 27: HL7 Standards- Segment
MSH - Message Header is required to communicate type of message
EVN - Identifies triggering event
PID - patient demographics.
PV1 - Patient Stay info.
PV2 - More Patient Stay info
NTE - free text comments or report data.

## Slide 28: HL7 Standards- Segments
Order Entry Specific Segments
  ORC –Transmits Common Order fields that may be grouped together.
  OBR – Defines specific test related data (Observation Request) and is used to transmit information specific to an order.
Result Entry Specific Segments
  OBX – Observation sends each individual result in a discrete mode. The OBX segment is used for SoftLab to transmit a single observation or result in a structured form.
NTE Segment- used by ADT, Order Entry, or Result interfaces to transmit textual data in a non-discrete format for Patient, Stay, Order, etc comments

## Slide 29: HL7 Standards- Data Fields
String of characters, separated from other fields by “|”
References to particular fields within a segment are indicated by [] i.e. OBR[18]

## Slide 30: HL7 Standards- Putting it all together

## Slide 31: MOM Message Oriented Middleware

## Slide 32: MoM (Message Oriented Middleware)
Software or hardware infrastructure
Supports sending and receiving messages between distributed systems.
Allows application modules to be distributed over heterogeneous platforms
Reduces the complexity of developing applications that span multiple operating systems and network protocols.
SCC utilizes MoM for integration with foreign systems, as well as integration between SCC applications.

## Slide 33: MoM (Message Oriented Middleware)

## Slide 34: MoM (Message Oriented Middleware)
Events in each application generate trigger events (Publish Event)
Publish Event pushed to MoM.
Trigger events/parent messages directed to data collectors to obtain information stored in the modules
Back to MoM.
Additional messages may be generated from MoM to obtain additional information
Routed to ESB for further processing and to be sent to internal/foreign systems (results reporting).

## Slide 35: MoM (Message Oriented Middleware)

## Slide 36: MoM (Message Oriented Middleware)

## Slide 37: Accessing MoM
Many ways to access:
1. SoftLab application Main screen Tools>MOM Console
2. SoftDMI application Main screen by selection of the DMI “url” located on the Status bar.
3. If the host and port are known, you can type in the “url” in your browser (Internet Explorer)

## Slide 38: Accessing MoM

## Slide 39: Copy Setup

## Slide 40: Copy setup
A utility which lets you copy multiple SETUP records between environments
Speeds up file building
Avoid human errors
Protect the integrity of records after copying.

## Slide 41: Environments
-The “From”
-By default, the environment from where Copy Setup launched.
-Can be changed by the user after launching Copy Setup.
-The “To”
-Possibly a choice of Targets.
-Choices would include:
-All compatible environments installed on the same PC.
-Those listed in SSM.
Source

## Slide 42
Access from Lab, Micro, or SecMan

## Slide 45: Search criteria
Search criteria from previous screens
List of available setups to copy
List of fields within the setup

## Slide 46: Example Search
Select all the active Doctors in TEST2 whose last name is Smith

## Slide 48: Example Search Results
Click on Compare

## Slide 50
Select the records you want to copy to the Target environment and click Add or Click Add All to copy all the records

## Slide 52: Example Records to Copy

## Slide 53: Check the record to copy it. Note the lock. Click Perform Copy
If a lock is present. this record becomes locked in the source and target environments. The record can be opened for reading in the source environment but it cannot be changed in the target until the lock is released

## Slide 54
After successful copy, this report will print to the screen.

## Slide 55: Unsuccessful Copy

## Slide 56: Unsuccessful Copy “Redo”
If you choose (and the differences are not too much), the system will allow you to copy the dependent records in addition to the one(s) you selected.

## Slide 57: Security (Only one option)
Option #799 on the Source and Target
(Copy Setup).
to “Read” to records on the Source
(search).
to “Read” to records on the Target
(comparison).
to “Edit/Add” to records on the Target
(copy).

## Slide 58: Settings and Definitions

## Slide 59: Settings and Definitions (SSM)
Main Menu/Setup/Settings and Definitions

## Slide 60: Finding SSM’s

## Slide 61: Finding SSM’s

## Slide 62: Editing SSM’s

## Slide 63: Editing SSM’s

## Slide 64: Editing SSM’s

## Slide 65: Editing SSM’s